## Slide 1: SP Office Gadget: Auto Door Unlocker
Hackware v3.0 (3 May 2017)
SP Digital Tech Talk (29 Dec 2016)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/sp-auto-door-unlocker

## Slide 2: Problem?
Tap staff pass on exit
  Trouble for visitors
  Hassle of taking out pass
Solution:
  Exit without tapping pass

## Slide 3: Demo Video
https://www.youtube.com/watch?v=IeWPlm1Xaz0

## Slide 4: Wireless remote unlocker
12V battery source
2 buttons
DIP code-select switch
Voltage-controlled oscillator (VCO)
  Frequency determined by voltage
330Mhz SMC5326P-3
  Some China chip
  Unknown function
  Cannot locate data sheet

## Slide 5: How the button triggers the signal?

## Slide 6: An electronic switch: Transistor
Control current flow with another current flow

## Slide 7: The trigger: Active IR + Ultrasonic Sensor
Ultrasonic HC-SR04 v2
  3.3V logic compatible
  Physical Domain
Infrared (IR) Distance Sensor GP2Y0A21YKR
  Effective range: 10 to 80cm
  Active IR
  Electromagnetic domain
=> Multi-modal integration / Sensor Fusion to avoid errors
Source: http://education.rec.ri.cmu.edu/content/electronics/boe/ir_sensor/1.html

## Slide 8: The brain: Microview
Microview = Arduino + 64x48 OLED screen
Runs on ATmega328P chip as with Arduino Uno
=
+
Source: http://makezine.com/2014/03/25/interview-with-marcus-schappi/

## Slide 9: Wireless Remote Modification
Extend button circuit (brown)
External 12V power (red and black)

## Slide 10: Assembly
Additional Components
  Breadboard
  12V DC Power Adapter

## Slide 11: Final Product

## Slide 12: Questions?
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/sp-auto-door-unlocker

## Slide 13: Control 12V signal with 5V
Source: https://electronics.stackexchange.com/a/70246
Microview 5V Logic Level
Remote is 12V Logic Level
-> Active-Low Dual NPN transistor